## Slide 1: AEROBRAKING AT MARS: A Machine Learning Implementation
Giusy Falcone
Zachary R. Putnam
Department of Aerospace Engineering
University of Illinois at Urbana-Champaign

## Slide 2
1. THE CONCEPT
Aerobraking, Autonomy, Goal & Challenges

## Slide 3: AEROBRAKING
Creation of drag is a function of velocity and flight-path angle
Propulsive maneuvers at apoapsis control velocity and flight-path angle
Aerobraking is a maneuver that uses successive passes through the upper atmosphere to dissipate orbital energy.

## Slide 4: IMPORTANCE OF AEROBRAKING & AUTONOMY
Benefits and Costs
Massive propellant saving WRT single propulsive maneuver at the expense of risk caused by variability in atmospheric density (heat rate & dynamic pressure)
Successfully performed for three Mars missions:
Mars Global Surveyor (1996)
Mars Odyssey (2001)
Mars Reconnaissance Orbiter (2005)
Importance of Autonomy
Ground cost, a team of engineers always-online, less aggressive conditions (more when orbital period decreases)
Previous efforts to address these issues with autonomy:
Aerobraking Autonomous Control (1999-2012)

## Slide 5: GOAL AND CHALLENGES
Perform a complete and successful autonomous aerobraking campaign at Mars with a learning and adaptive behavior approach while:
1. Satisfying constraints on dynamic pressure and heat rate
2. Managing mission risk
3. Minimizing control effort and time of flight (cost)

## Slide 6
2. PROBLEM FORMULATION
Mission Modeling, Reinforcement Learning and Interface

## Slide 7: AEROBRAKING MISSION MODELING
Aerobraking mission: vary periapsis altitude to lower apoapsis altitude while satisfying constraints
Keplerian Trajectory Simulator
Aeroassist Simulation
rao
rpi
vi, fpai
rai, dpi, hri
Autonomy

## Slide 8: REINFORCEMENT LEARNING
Tabular Q-Learning Algorithm with ε-greedy policy search
<S, A,P ass’, R ass’, γ >
S = apoapsis radius
A = periapsis altitude
R ass’ =reward built to minimize the aerobraking whole time.
Reinforcement learning is learning what to do…so as to maximize a numerical reward signal. (Sutton)
“

## Slide 9: INTERFACE BETWEEN MISSION AND RL
A trained policy chooses when perform a trim maneuver to minimize the aerobraking time and to avoid the violating constraints.

## Slide 10
3. RESULTS
Aerobraking Simulation, Constraints & Corridor, Learning

## Slide 11
AEROBRAKING SIMULATION
Apoapsis radius from 200,000 km to 5,000 km
PERIAPSIS

## Slide 12: CONSTRAINTS AND CORRIDOR
NOT TRAINED MACHINE
TRAINED MACHINE
# Orbit
# Orbit
# Orbit
# Orbit

## Slide 13: RESULTS DELTA-V AND TOTAL TIME
REWARD FUNCTION DECREASES ONLY TOTAL TIME

## Slide 14
LEARNING PROCESS
Reward:
If reach goal
If heat rate and dynamic pressure closer to corridor boundary (dynamic)
Penalty:
If overcome heat rate (0.4 W/cm2), dynamic pressure (0.4 N/m^2)
If escape/impact
If apoapsis radius does not variate

## Slide 15: THANKS!
Any questions?
You can find me at:
gfalcon2@illinois.edu

## Slide 16: REFERENCES
J. L. Hanna, R. Tolson, A. D. Cianciolo, and J. Dec, “Autonomous aerobraking at mars,” 2002.
J. L. Prince, R. W. Powell, and D. Murri, “Autonomous aerobraking: A design, development, and feasibility study,” 2011.
J. A. Dec and M. N. Thornblom, “Autonomous aerobraking: Thermal analysis and response surface development,” 2011.
R. Maddock, A. Bowes, R. Powell, J. Prince, and A. Dwyer Cianciolo, “Autonomous aerobraking development software: Phase one performance analysis at mars, venus, and titan,” in AIAA/AAS Astrodynamics Specialist Conference , 2012, p. 5074.
D. G. Murri, R. W. Powell, and J. L. Prince, “Development of autonomous aerobraking (phase 1),”2012.
D. G. Murri, “Development of autonomous aerobraking-phase 2,” 2013.
Z. R. Putnam, “Improved analytical methods for assessment of hypersonic drag-modulation trajectory control,” Ph.D. dissertation, Georgia Institute of Technology, 2015.
A. Geramifard, T. J. Walsh, S. Tellex, G. Chowdhary, N. Roy, J. P. How et al. , “A tutorial on linear function approximators for dynamic programming and reinforcement learning,” Foundations and Trends® in Machine Learning , vol. 6, no. 4, pp. 375–451, 2013.
J. L. H. Prince and S. A. Striepe, “Nasa langley trajectory simulation and analysis capabilities for mars reconnaissance orbiter.”
V. Mnih, "Playing atari with deep reinforcement learning." arXiv preprint arXiv:1312.5602 (2013).
R.S . Sutton, and A. G. Barto. “ Reinforcement learning: An introduction. “, Vol. 1. No. 1. Cambridge: MIT press, 1998.
M. Techlabs, “ Picture Reinforcement Learning Explanation. “, Retrieved from https://goo.gl/images/JTxJpf

## Slide 17: MISSION DESIGN CHARACTERISTICS
Small Satellite
Mass: 110 kg
Drag Area: 10 m2
CD: 1.2
Keplerian Trajectory
Simulator (2-bodies)
Aeroassist Simulator
3 DOF equations of motion. Numeric simulation integrated using a forth order Runge-Kutta scheme.
Density model: Mars-Gram 2010

## Slide 18: REINFORCEMENT LEARNING
Markov Decision Process (stochastic):
<S, A,P ass’, R ass’, γ >
S = state space (apoapsis radius)
A = action space (periapsis altitude)
P ass ==probability of getting into s′ after a from s
R ass’ =expected reward from s to s’ after a
Find policy π* through iteration Bellman eq.

## Slide 19: MDP
STATE SPACE
Apoapsis radius
From 4000 to 400000 km.
981 states.
ACTION SPACE
Periapsis altitude
From 105 to 127 km.
147 states.
REWARD FUNCTION
Reward:
Reach goal.
If closer to corridor boundary (dynamic).
Penalty:
Overcome heat rate (0.4 W/cm2), dynamic pressure (0.4 N/m^2).
Escape/Impact.
If apoapsis radius does not variate.

## Slide 20: Q-LEARNING ALGORITHM
Off-policy and model free algorithm

## Slide 21: ε-GREEDY POLICY SEARCH
ε-greedy policy spans between exploration and exploitation:
• With probability 1- ε, uses the greedy action:
• With probability ε, play random action.